## Slide 1: Silence in the Spectrum: Unmasking Speech From Noise
Junze Xie | Ming Chen | Zifan Xu | Yimin Chen | Wanting Luo
Signals, Systems & Probability

## Slide 2: 01 Table of contents
Background & Problems
Advancing:
Wiener Masking
Signal Model & Baseline Filter
Results & Evaluation
02
03
04
2

## Slide 3: 01 Background & Problems
Voice Denoising in
Physical Environment

## Slide 4: Scenario
In a public setting
Such as a train station
A phone call came through
4

## Slide 5: Scope
A voice signal affected by high-frequency hiss in public environment.
simulated signal
Physical signal

## Slide 6: Problem Statement
Clean Voice
Hiss Noise
Noisy Voice
Denoising System
Enhanced Voice
Goal: remove the noise from background and preserve the voice from user.
6

## Slide 7: 02 Signal Model & Baseline Filter
Fundamentals of Speech Denoising

## Slide 8: Signal Model
—
The clean and hiss voise are both signals.
—
—
The noisy voice is a
superposition.
The filter is an
input-output system.
Frequency response illustrates what the system keeps or suppresses.
8

## Slide 9: Frequency-Domain Observation
Clean Voice
Hiss Noise
Low Frequency
High Frequency
Discrete Fourier Transform
9

## Slide 10: Frequency-Domain Observation
Clean Voice
Hiss Noise
Low Frequency
High Frequency
10

## Slide 11: Low-Pass Filter
Low-pass filter keeps lower frequencies and attenuates higher frequencies.
11

## Slide 12: Parameter Choice
Trade-off !
Lower cutoff: stronger noise reduction, but speech suffers more.
Higher cutoff: more speech detail, but more hiss remains.
12

## Slide 13: Shortage of low-pass filter
It does not know the signal is speech-dominant or noise-dominant.
Low-pass uses the same attenuation for the entire signal.
This can reduce hiss, but it can also remove useful speech detail.
This motivates a more flexible method.
13

## Slide 14: 03 From Fixed to Adaptive
From fixed filters to adaptive time-frequency masks

## Slide 15: Frequency-Domain Masking
Dominated noise means strong reduction.
Specified gains to each frequency bin.
Dominated speech means little attenuation.
The mask changes with both time and frequency.
M ≈ 0
M ≈ 1
Y(f) = H(f)X(f)
Y(t,f) = M(t,f)X(t,f)
15

## Slide 16: Short-time Fourier Transform
16

## Slide 17: Frequency-domain mask
Frequency-domain masking makes local decisions and can better balance noise reduction with speech clarity.
17

## Slide 18: Wiener-Style Mask
Adaptive Behavior
Different frequencies receive different gain values instead of using one fixed cutoff.
Practical Benefits
This often gives better clarity than simple low-pass filtering while still reducing hiss noise
18

## Slide 19: The Pipeline of Our System
From fixed filters to adaptive time-frequency masks
19

## Slide 20: Demo
- - - - - - - - - - - - - - - - - - - - - - - - - - - - - -
Reference of the original speech
1. Clean voice
2. Noisy voice
- - - - - - - - - - - - - - - - - - - - - - - - - - - - - -
Speech mixed with
hiss noise
3. Low-pass result
- - - - - - - - - - - - - - - - - - - - - - - - - - - - - -
After low-pass filtering:
noise reduced, but some
speech details lost
4. Mask result
- - - - - - - - - - - - - - - - - - - - - - - - - - - - - -
After mask filtering:
noise suppressed while
speech details preserved
20

## Slide 21: Result comparison
Noisy voice spectrogram
Low-pass result spectrogram
Mask result spectrogram
21

## Slide 22: A simple filter can become a richer system
Conclusions
Signals and Systems Perspective
01
Baseline: Low-pass Filtering
Low-pass filtering provides a simple baseline by removing
high-frequency noise.
02
Frequency-Domain Masking
Allowing different gains for different frequencies.
03
Wiener-Style Mask
Designing frequency-dependent attenuation based on the power of speech and noise.
04
Modeling the voice denoising as a Signals and Systems problem.
22

## Slide 23: Thanks!
Junze Xie | Ming Chen | Zifan Xu
Yimin Chen | Wanting Luo